## Slide 1: Neural networks Applied to structure Health monitoring
Felipe da Costa Pereira

## Slide 2: paper
https://doi.org/10.1111/j.1467-8667.2010.00685.x
Structural Health Monitoring (SHM);
Autoregressive Models as features extraction technique for damage detection:
    Optimal Model order estimation
Datasets are measurements from a Laboratory test structure under different environments and failure conditions;

## Slide 3: experiment
Measurements
(features)
Bumper:
damage
Environmental conditions:
Mass addition
Columns stiffness variation
Group 1
Group 2
Group 3
Group 4

## Slide 4: Feature extraction the autoregressive model
“Time-series analysis takes into account the fact that data points sampled over time may have an internal structure, such as autocorrelations, trends or seasonal variations…
The second SHM approach consists of fitting an AR model to signals from the undamaged and damaged structural conditions. In this approach, the AR parameters are used directly as damage sensitive features, and some form of a multivariate classifier can be used to distinguish between the damage classes.
The appropriate AR model order is initially unknown. A higher order model may better fit the data but may not generalize well to other data sets.
On the other hand, a low-order model will not necessarily capture the underlying physical system dynamics.”

## Slide 5: Feature extraction the autoregressive model
Conclusions based on statistical approach:
- 15<p<30: capable of discriminating the undamaged and damaged state conditions, even in the presence of simulated operational and environmental variability.
- If p<15: no guarantee to distinguish all the undamaged and damaged state conditions when the operational and environmental variability was included in the experiments.
- AR modeling can be an effective feature extraction technique when the damage introduces non linearities and the operational and environmental variations manifest themselves as linear system changes.

## Slide 6: Dataset
{ }
850
Experiments
(cases)
4 x 8192 features
X =
Y =
(17 classes)
{ }
850
(4 x p) features = 120
XAR =
850
{}
label
time series
Ø
Exploratory analysis
Histograms
Dimensionality Reduction
Supervised Model
Feature selection
Unsupervised (secondary objective)
Neural Network for classification
Series plot
Cross plots
Self Organized Map
Apply AR(p) model
PCA
Data Scaling
Feature Extraction
Validation
Train/Test split
K-fold cross validation
Test different architectures
Group similar damage types
workflow

## Slide 7: Objectives
Main Objectives:
  Train an artificial neural network as a classifier to predict the class of damage
  “Test” ANN different architectures to improve its performance
Secondary Objectives:
  Compare ANN vs :
    Soft-classifiers (SVM, k-nn, Softmax, Naïve Bayes, Decision Trees, etc)
    Ensemble methods (Boosting, Bagging, etc)
  Train a Self Organizing Map to explore relation between