## Slide 1: Neural Networks applied to Structure Health Monitoring using autoregressive models as feature extractors
Felipe da Costa Pereira – mat. 2212376 - ELE2389

## Slide 2: Problem description
Structure Health Monitoring (SHM): detect damage on a given physical system
Data: measures of accelerometers on laboratory assembly(*1)
Different damage and environmental conditions (*1)
Autoregressive (AR) Models as feature extractors from timeseries measures(*2)
Objectives:
  train a MLP Neural Network as a classifier to predict the classes of damage (state conditions);
  compare its results with other popular algorithms for classification;
  train a self-organizing map to explore the feature space and the relations between state conditions;
(*1) [Figueiredo et al., Structural health monitoring using standard data sets - report, 2009]
(*2) [Figueiredo et al., Computer-Aided Civil and Infrastructure Engineering, 26(3):225–238., 2011]

## Slide 3: Data processing pipeline

## Slide 4: Dataset and feature extraction
Original Dataset:
Cases: 850 (17 conditions x 50)
Features: 4 timeseries x 8192 datapoints
Group 1
(Baseline)
Group 2
(Environmental
Change only)
Group 3
(Damage only)
Group 4
(Damage +
Envoronmental change)
After AR Model:
Cases: 850 (17 conditions x 50)
Features: 4 channels x 30 AR coefficients
1
AR model (p=30)
2
Concatenation
After concatenation:
Cases: 850
Features: 120 AR coefficients
4 sensors timeseries
case #790, label#16
Ch1
Ch2
Ch4
Ch3
3

## Slide 5: Exploratory analysis
Correlation Matrix (AR Model)
PCA transform explained variances
PCA 1
PCA 1
PCA 1
PCA 2
PCA 3
binary
4 groups
17 states
High correlation specially channels 1 and 2
PCA compression: 6 components representing 96% variance

## Slide 6: Neural network (MLP)
Model validation protocol
Confusion Matrices (normalized by true label)
4 groups vs 17 state conditions prediction
best accuracy = .965
Average = .956
best accuracy = .971
Average = .925
Similar performance in predicting either 4 group of 17 state conditions
Chosen model: 6 input, 13 hidden neurons (1 hidden layer)
Relu activation (hidden layer) and softmax activation (output)

## Slide 7: Soft models

## Slide 8: Classifiers Results
Neural Network, linear models (SVM and Logistic Regression - Softmax) showed a better performance;
Some classifiers performed worse than the Naïve Bayes Classifier
Poor performance for the AdaBoost, Bagging and Decision Trees algorithms
Stacking classifier was the best among ensemble methods;

## Slide 9: Self organizing map Results
The self organizing map trained in this example (12x15) was not complex enough to map the features in 4 or 17 groups
12x15 som
Binary class labels
17 state conditions labels
4 groups labels

## Slide 10: Self organizing map Results
The self organizing map trained in this example (25x25) can capture the four gourps and some of the 17 state conditions

## Slide 11: Concluding remarks
AR models, when using an appropriate order, are indeed useful as a feature extractor and its coefficients can be used as features in the new input space. [Figueiredo et al., 2011]
For the proposed problem, the PCA technique was responsible for achieving a high compression transforming a 120-dimension input space into a 6-component with only a few loss of information.
The neural network model as well as the other classifiers (specially the linear models) performed well in detecting damage in the studied laboratory structure, considering the pre-processing procedures implemented (feature extraction and dimensionality reduction).
It’s reasonable to think that the same neural network or any of the soft classifiers, if applied directly to the initial feature space would lead to a poor performance as classifiers, due to the huge number of features, what shows the importance of the preliminary steps in a data processing pipeline.
Self-Organizing Map trained in this study was capable of capturing the groups at a high level (binary classification: damaged vs undamaged), but showed a weak performance when getting in more detailed classification